## Slide 1: Climate resilience through distributed shared data
Amit Bhave
CMCL
Gemini Call
12 September 2023
Notes: 42s
Hello, I’m Amit Bhave, and I am from CMCL.
Thanks to the team at DT Hub for this opportunity to present at today’s Gemini Call.
Today, in line with the release of the technical reports and a new video from CMCL, I'm going to provide a brief technical overview of CReDo
CReDo i.e. Climate Resilience Demonstrator is a connected digital twin, and the team at CMCL led the technical development and implementation of many parts of CReDo.
At CMCL, our mission is to enable cross-domain interoperability

## Slide 2: CReDo is a climate change adaptation digital twin
        Bringing together data across energy, water, and telecoms networks​
  Anglian Water’s water and sewerage assets
  BT and Openreach’s communication assets
  UKPN’s power network assets
  NHS/healthcare infrastructure
        With flood data to understand…
  Infrastructure interdependencies
  Asset failure and combined system impact
  What can we do to prepare or respond?
How do we increase system resilience and adapt?
Notes: 50 s
CReDo is a climate change adaptation digital twin designed to address the cascading risks across infra networks, highlighted by the Joint Committee on National Security.
It brings together data across different networks such as energy, water, telecoms and hospital infrastructure., together with flood data and scenarios to understand:
Infrastructure interdependencies
Asset failure and combined impact across systems or networks
“How do we increase system resilience and adapt to climate change”?
To address this questions, we take a “network of networks” or a “system of systems” approach.
Today, I would like to touch upon the following three aspects:
data structure we used.
The adoption of distributed architecture and the technical solution
A short use case via the CReDo visualisation.

## Slide 3: Data structures
Core concepts
Description
Elevation
Boundary
Point location
Flood State
Flood Depth
Site
Asset
Asset Owner
Asset Property
State
Notes: 41s
The internal data structure used by CReDo is based on a hierarchy of simple ontologies.
At the top of the hierarchy we define concepts and relationships about asset and flood data that apply throughout CReDo.
The slide illustrates some of the main concepts and relationships. The concepts are the nodes, and the relationships are the arrows in the diagram.
An asset will have an owner and a set of properties describing the flood, the operational state of the asset and its location etc.
An asset may also supply something, for example power, to an asset, represented by the green arrow.

## Slide 4: Knowledge graph
Connected data and insights
Secondary
Substation
Primary
Substation
Secondary
Substation
Secondary
Substation
Secondary
Substation
Secondary
Substation
Primary
Substation
Cabinet
Exchange
Mobile
Water Subsite
Water Subsite
Sewage Subsite
Sludge Subsite
Notes: 24s
When we use these ontologies to represent data we form a directed graph.
The instances of the concepts – in this case the assets – form the nodes of the graph, while the relationships between concepts – in this case the supplies relationships – form the arrows between nodes.
This is the basis of how we form the CReDo knowledge graph…

## Slide 5: Knowledge graph
Connected data and insights
Notes: 23 s
…and is reflected in the connectivity of the assets on the CReDo visualisation. [CLICK].
In CReDo, we use computational agents that operate on the knowledge graph to describe the response of each asset to flooding, and to resolve the cascade of failures throughout the combined network.
Thus, we can interoperate across the instances, i.e. enable interoperability between data from different networks.

## Slide 6: Technical solution
Resolve connectivity, process climate data and failure models, manage scenarios
Data and service providers
Encrypted communication
Separation of data
Secure by design with need-to-know access
Anglian Water’s servers
BT’s servers
UKPN’s servers
Other asset owner servers
Other data sources
Climate projection and flood data
Other models
Distributed Architecture
Notes: 70 s
This diagram shows the distributed architecture.
Starting on the right-hand side, the asset owner data is hosted securely on separate servers (provided by STFC within the DAFNI infrastructure).
Each server runs a separate visualisation, providing a means to facilitate different views of the insights and data.
In the middle of the diagram is a central node, responsible for:
• resolving the connectivity between assets.
• simulating asset failures and the impact across the combined network.
• and, managing scenarios, so for example which combinations of climate and asset data are analysed.
On the left-hand side of the diagram, we connect to data and service providers. For example:
• Climate projection and flood data, which has been provided by Fathom in Phase 2.
• Other models, for example to assess the economic consequences of a scenario and recommend possible actions to improve resilience.
• And other data sources, for example data about NHS infrastructure.
The vision is of an extensible system, where multiple providers can offer models and data.

## Slide 7: Journey towards connected digital twins
Ecosystem Distributed Architecture
Energy
Telecoms
Climate data
Transport
Health
Manufacturing
Water
Notes: 11s
…and this is very much aligned with the vision of the Ecosystem Distributed architecture, thus enabling a shared understanding across various sectors such as transport, health, manufacturing, etc.

## Slide 8: Shared data enables connected understanding
Notes: 23 s
Consider a weather event such as a flood that has compromised assets from the energy network, this can in turn have a knock-on impact on other sectors. The other networks, however, may not be aware that they are vulnerable to this cascading risk.
Thus, by analysing shared data we develop a connected understanding of the overall system.

## Slide 9: System-Wide View – nhs
Anglian Water’s servers
BT’s servers
UKPN’s servers
Other asset owner servers
Notes: 30 s
In the event of a suitable data sharing agreement that allows connections to all the servers, it is possible to retrieve the system-wide view of the overall connected infrastructure network, including new asset owners, for example the critical healthcare infrastructure.
This system-wide view may be useful to asset owners and regulators alike

## Slide 10
Notes: 27 s
Here’s a snapshot of the CReDo visualisation.
Red rings around the asset denote direct failure due to flooding and orange ring indicates indirect failure. Diff. types of flooding, for example, pluvial, fluvial and coastal are considered.
Let’s consider a scenario where the power, water, telecoms and healthcare infrastructure experience a 1 in 1000 yr flood event.

## Slide 11
Selected site
Metadata about asset
State of asset
State of connections
Connectivity of asset
Notes: 13 s
On selecting a failed asset site, additional information regarding the location of the asset, the flood state of the asset, the state of connections and connectivity of the asset is displayed to the user.

## Slide 12
Primary sub-station 01 indirectly supplies two hospitals
Notes: 22 s
For example, in the area highlighted, the primary substation supplies power to two NHS hospitals in the region
One of the hospitals (marked by a red circle) has directly failed and lost power and telephone service.
The second hospital has not flooded but is experiencing indirect failure.

## Slide 13
Primary sub-station 01 indirectly supplies two hospitals
Notes: 15 s
An alternative scenario suggesting investments to improve the resilience of the power substation shows an option to avoid the loss of power for both hospitals.

## Slide 14
Primary sub-station 01
Notes: 18 s
CReDo also offers an analytics dashboard that derives and summarises information across multiple scenarios, providing a simple view of complex information to support decision making.
Examples include a list of assets with the highest vulnerability and economic information regarding potential interventions, etc.

## Slide 15: Project partners
Acknowledging Phase 1 contributors
Centre for Digital Built Britain | Joint Centre for Excellence In Environmental Intelligence | Department for Business, Energy & Industrial Strategy | National Digital Twin Programme
Cambridge University | Crocodile Media | Mott MacDonald | ESRI UK
Notes: 11 s
I would like to acknowledge the partners and contributors to the multiple phases of CReDo.
Thank you for your attention.